## Slide 1: Reakce rafinérsko-petrochemického komplexu na budoucí výzvy v rámci Green Deal
25/11/2021
datum:
jméno:
Jiří Hájek, ředitel a předseda představenstva, ORLEN UniCRE

## Slide 2
Fuels production vision 2050

## Slide 3
Utilization of new attractive opportunities
Hydrogen
Advanced biofuels (biogenic and municipal waste)
Renewable sources of energy
Waste plastic recycling
Bio-products from existing refinery asset
Bio-petrochemicals and recycled polymers
Steam-gas energy block
Green NH3 as energy caries
E-mobility

## Slide 4
Biofuels production
Ambition:
RED II (III) compliance;
Reduction of carbon footprint related to automotive, marine and aviation fuels utilization;
Focus:
Forest and agriculture residuum, municipal waste;
Key challenges:
        Waste biogenic feedstock provision → effective collection, storage, analysis, pretreatment;
        Technology maturity → TRL level, feedstock flexibility, feed quality sensitivity, yield of desired products, energy and hydrogen consumption, undesired product/waste utilization;
        Co-processing vs stand alone installation;
        Blending potential with existing fuels → RON, CI, stability, oxygen content;

## Slide 5
COMSYN process concept
Main Targets :
Concept: decentralized primary conversion of biomass in 30 – 150 MW units.
Target: reduction of biofuel production cost up to 35% compared to alternative routes → production cost for diesel lower than 0.80 €/l.
GHG savings: 80 %
Overall efficiency to FT biocrude + heat: 80%

## Slide 6
Simulation processing in existing refinery
FT WAX >10 wt.%
80% reduction in the GHG emissions was reached for studied case
84 wt. % of FT Oil+Wax is converted to motor fuels.
14 wt. % of FT Oil+Wax is converted to Steam cracker feedstock.
2.6 wt. % of FT Oil+Wax converted to fuel gas
Obtained Production cost for biofuel is 1.10 EUR/l
The Break-even price of FT Biofuels after refining upgrade is at 1.7 EUR/kg
BENEFIT
No benefit
CURRENTLY
Green NH3 as energy caries
Notes: The real break-even price of FT Biofuels produced from FT Wax+Oil has to include the effects associated with the fact that 14 % of feed is lost in Steam cracker feed pool and 2,6 % feed is lost in Refinery Fuel Gas.
Due to the current plastics EU policy and customers requirements (Unipetrol´s customer survey), side products used for basic-plastics Production (polyethylene, polypropylene) and fuel gas have to be priced with a significantly lower value (as a fossil equivalent) than purchase cost of FT WAX+Oil.

## Slide 7
Chemical recycling of waste plastics & EoL tires
To develop/implement concept of chemical recycling via pyrolysis scalable to production capacities of from 90 ktpa (2030) to 180 ktpa (2040) of pyrolysis oil.
Project description:
Current status:
Challenge 1 – dialogue with waste management sector – ongoing.
Challenge 2 (refer to roadmap in appendix section) – all options under development (lab-scale PoC), joint activity with ORLEN CG (Case Razem/Spolu).
Challenge 3 – bussines cases in preparation, first PIMS calculations carried out, characterisation methods developed.
Focus on key challenges:
Establish strategic partnerships with waste management sector  Challenge 1 – sourcing the feedstock.
Remove „high“ risk contaminants (fluorine, chlorine, bromine, metals)  Challenge 2 – technology itself:
  Option 1 – „smart pyrolysis“ – in-house or external technology.
  Option 2 – „on-line“ dehalogenation.
  Option 3 – „off-line“ dehalogenation.
How to plan utilisation of current/new assets to achieve the most cost-effective solution for chemical recycling with short time-to-market  Challenge 3 –asset management with chemical recycling.
Opportunities:
To introduce sustainable feedstock into production of petrochemicals (company level).
Recognize responsibility and offer solution for sustainable plastics (company + global level).
Reduce GHG emissions from waste plastic incineration (global level).
Key enablers? Solving following challenges:

## Slide 8
Hydrogen Eagle – green hydrogen for CEE

## Slide 9
LCA of ICE / BV / FCV
ICE
BV
FCV
Total life cycle emission
g CO2 / km
Vehicle production and post-treatment
g CO2 / km
Production, distribution and energy consumption
g CO2 / km
Chart: 
 | 140
 | 70
Chart: 
 | 10
 | 90
Chart: 
 | 20
 | 100
as per energy source, higher efficiency then FCV
as per the source of energy and hydrogen production technology
mainly production and combustion of fossil fuels
Chart: 
 | 180
 | 90
Chart: 
 | 160
 | 110
Chart: 
 | 130
 | 100
future reduction via new ECO friendly batteries with higher recycling potential
dynamic development, future emission reduction
lowering (mainly advanced)
160-250
130-230
180-270
10-100*
20-120
140-210
Chart: 
 | 40
 | 20
Chart: 
 | 150
Chart: 
 | 110
battery production and limited recycling potential
battery Production and carbon fibers in high pressure vessels
relatively lowest
~ 150
~ 110
40-60
* Emission during life cycle relay on energy source where coal represents the highest and RES the lowest.
Source: Deloitte, Ballard – Fueling the future of mobility, 2020

## Slide 10
PRODUCER
CUSTOMER

## Slide 11: Thank You for Your attention